## Slide 1: Robot Catchers
An overview of the current state of the art
Tom Queen
Daniel Turner
Demetrius Zaibo

## Slide 2: Catching Robots
What are they?
  Machines which automatically grasp or intercept a target moving object
How could they be useful
  Toys
  Sports training
  Robotic assistants on space walks
  Impromptu conveyor systems over uneven terrain

## Slide 3: Design Challenges: Hardware
Body Design
  Effective work area
  Strength, speed and safety
  Power consumption
Gripper Design
  Catchable objects
  Post-catch manipulation
  Control complexity

## Slide 4: Design Challenges: Visual Feedback
Camera Setup
  Influences required processing power
  Feedback accuracy, precision and frequency
  System complexity
Object Tracking
  Object recognition and categorisation
  Feedback reliability
  Algorithm processing efficiency

## Slide 5: Design Challenges: Control
Gripper-Object Coordination
  Body kinematics and control
  System reliability
Object Grasping
  Training
  Object models
  No generic solution
Notes: As is the case with such complex problems, many different designs have been made in order to solve them. Each with their own benefits and costs.
To get a better feel for the state of the art, we’ll briefly analyse some of the more common solutions for each of the challenges.

## Slide 6: Design Solutions: Body Designs (Arms)
Industrial Arms:
  Strong, fast, and standardised
  Expensive, fixed workspace, and human unfriendly
Humanoid:
  Safe(r) and can mimic humans
  Expensive, complex control
Pendulums
  Simple design, cheap
  Small, fixed workspace

## Slide 7: Design Solutions: Body Designs (Supports)
2-Axis Frames
  Simple design and control
  Limited workspace, bulky
Delta Frames
  Simple control, large workspace
  Bulkier, many moving parts
Flying Nets
  Massive workspace with a very simple design
  VERY complicated control

## Slide 8: Design Solutions: Gripper Designs (Passive Vs Active)
Active grippers have an element of control
  Allows for manipulation of objects post-catch
Passive grippers trade control for simplicity
  Usually lighter weight, no cables required!

## Slide 9: Design Solutions: Gripper Designs (Soft Vs Hard)
Hard grippers are prevalent in industry
  Standardised, simple and well tested
Soft grippers are prevalent in nature
  Deformable, safe and versatile

## Slide 10: Design Solutions: Camera Setups
Eye in hand
  Simple feedback systems
  Increased gripper design complexity
Head camera(s)
  Improved object tracking
  Increased control complexity
Room camera(s)
  Excellent object tracking
  Complex robot setup, more processing required

## Slide 11: Design Solutions: Object Tracking
Colour
  Simple algorithms
  Limited to known items, many false positives
Structure
  More complex algorithms
  Limited to known items
Depth
  Not limited to certain items
  Larger hardware and computational costs

## Slide 12: Design Solutions: Gripper-Object Coordination
Kinematic Models
  Standardised solutions, e.g. ROS
Predictive Feedback
  Can intercept via predicting object trajectories
Visual Servoing
  For eye-in-hand and grid-based setups direct (reactive) feedback loops are possible

## Slide 13: Design Solutions: Object Grasping
Open Problem!
  Active area of research
  Usually train with known objects and constrained throwing (e.g. object won’t spin)
  Often just ignored with passive robotics

## Slide 14: Summary
Catching robotics is an active area of research
Many solutions are being tested
Most challenges cross-over into other areas of research, e.g. visual processing
Grasping and manipulating objects is hard

## Slide 15: Questions?